## Slide 1: BGP-PCEP Tutorial
ODL Summit, Seattle - Sept 2016
Ajay Chhabria
Ajay Lele
Kevin Wang
Brocade
Giles Heron
Cisco

## Slide 2: Agenda
Setup Creation
BGP
  BGP IPv4/IPv6 Routes
  BGP-LS
  Application Peer
  OpenConfig
PCEP
  PCE initiated LSPs
  PCC initiated LSPs (Delegation)
  Bandwidth Update
  Segment Routing
BMP
Flowspec

## Slide 3: Pre-requisites
Basic understanding of BGP and PCEP protocols
Familiarity with ODL
Resources
  Laptop with sufficient resources to create VM

## Slide 4: Setup Creation

## Slide 5: Lab Network Diagram
AS: 65504
SJC
LAX
Controller
SAN
SFC
MIN
KCY
POR
SEA

## Slide 6: Setup Components
VIRL Network Simulation
Cisco dCloud
Conference Center
OpenDaylight Controller
Anyconnect VPN
Controller VM
OpenDaylight Lab

## Slide 7: Controller VM
Three options for creating Controller VM
  Use preconfigured VM from USB stick
  (login: odlsummit/odlsummit)
  Use Vagrant to launch preconfigured VM
  (login: vagrant/vagrant)
  Use any vanilla VM and configure manually
Use ODL setup scripts for configuration https://github.com/kevinxw/opendaylight-setup
  Install OpenDaylight Controller
  Initialize Controller
  Connect to dCloud session using Anyconnect VPN

## Slide 8: Network Simulation
Simulated network will be run in Cisco dCloud using VIRL
For today sessions will be pre-launched and run from Giles’ account.
Register and login to dCloud https://dcloud.cisco.com/
Search for “OpenDaylight Boron with Apps with 8 Nodes”
Schedule and launch lab session

## Slide 9: Setup Verification
Controller VM configured and ODL process running
dCloud Lab status page shows all steps completed and in green
Ping from Controller VM to SJC router successful

## Slide 10: ODL BGP/PCEP Plugins

## Slide 11: ODL BGP/PCEP Overview
OSPF
OSPF
BGP
Core
Edge
Route Reflector
Core
Edge
Route Reflector
Edge
Edge
BGP
Link-State, IPv4, IPv6, Labelled Unicast, IPVPN, EVPN and Flowspec routes
MPLS LSPs via PCEP
Edge
BGP
PCE-P
OSPF
OSPF
PCE-P
OSPF
BGP
OSPF
BGP
OSPF
OSPF
OSPF
BGP
App
PCE-P
RESTCONF
BGP
Topology

## Slide 12: BGP/PCEP Topologies
Link-State
IPv4
IPv6
PCE-P
BGP
RR
BGP
BGP
OSPF
OSPF
OSPF
OSPF
OSPF
OSPF
BGP-LS

## Slide 13: BGP

## Slide 14: Overview
Exterior Gateway Protocol, used to exchange routing information between Autonomous Systems
Explicit connection establishment between peers (EBGP, IBGP, RR)
No periodic routing updates; sent only when information changes
MP-BGP enables supports for multiple address families
One or more attributes associated with prefixes; policies are applied on these attributes
Message Type | Description
OPEN | Exchange of options & capabilities
KEEPALIVE | Heartbeat message, Dead peer detection
UPDATE | Transfer routing information
NOTIFICATION | Inform about exception conditions
ROUTE-REFRESH | Request peer to re-send routing information

## Slide 15: Standards Supported
RFC4271 - A Border Gateway Protocol 4 (BGP-4)
RFC4456 - BGP Route Reflection: An Alternative to Full Mesh Internal BGP (IBGP)
RFC1997 - BGP Communities Attribute
RFC4360 - BGP Extended Communities Attribute
RFC4486 - Subcodes for BGP Cease Notification Message
RFC5492 - Capabilities Advertisement with BGP-4
RFC5004 - Avoid BGP Best Path Transitions from One External to Another
RFC6286 - Autonomous-System-Wide Unique BGP Identifier for BGP-4
RFC6793 - BGP Support for Four-Octet Autonomous System (AS) Number Space
RFC7311 - The Accumulated IGP Metric Attribute for BGP
RFC5668 - 4-Octet AS Specific BGP Extended Community
draft-ietf-idr-link-bandwidth - BGP Link Bandwidth Extended Community
draft-ietf-idr-bgp-extended-messages - Extended Message support for BGP

## Slide 16: Standards Supported
RFC4760 - Multiprotocol Extensions for BGP-4
  RFC2545 - Use of BGP-4 Multiprotocol Extensions for IPv6 Inter-Domain Routing
  RFC7752 - North-Bound Distribution of Link-State and TE Information using BGP
    draft-gredler-idr-bgp-ls-segment-routing-ext - BGP Link-State extensions for Segment Routing
    draft-ietf-idr-bgpls-segment-routing-epe - Segment Routing Egress Peer Engineering BGP-LS Extensions
  RFC5575 - Dissemination of Flow Specification Rules
    RFC7674 - Clarification of the Flowspec Redirect Extended Community
    draft-ietf-idr-flow-spec-v6 - Dissemination of Flow Specification Rules for IPv6
    draft-ietf-idr-flowspec-redirect-ip - BGP Flow-Spec Redirect to IP Action
RFC3107 - Carrying Label Information in BGP-4
  draft-ietf-idr-bgp-prefix-sid - Segment Routing Prefix SID extensions for BGP
RFC4364 - BGP/MPLS IP Virtual Private Networks (VPNs)
  RFC4659 - BGP-MPLS IP Virtual Private Network (VPN) Extension for IPv6 VPN
RFC7432 - BGP MPLS-Based Ethernet VPN
  draft-ietf-bess-evpn-overlay - A Network Virtualization Overlay Solution using EVPN
  draft-ietf-bess-evpn-vpws - VPWS support in EVPN
RFC7911 - Advertisement of Multiple Paths in BGP
RFC2918 - Route Refresh Capability for BGP-4

## Slide 17: Processing of Routes
BGP Peer 1
ODL BGP Speaker
BGP Peer 2
Adj-RIB-In
Loc-RIB
Adj-RIB-Out
Export
Policy
Adj-RIB-In
Adj-RIB-In
Adj-RIB-Out
Adj-RIB-Out
Import
Policy
Topology
Exporter
IPv4/IPv6 Reachability Topology
Linkstate
Topology
Effective-RIB-In
Effective-RIB-In
Decision
Process
Effective-RIB-In
App-RIB
RESTCONF
External App
Import
Policy

## Slide 18: BGP RIB Model
List of RIBs, indexed by an ID
Note: config  false
List of peers, indexed by peer-ID
Peer role: ebgp, ibgp, or rr-client
Adj-RIB-In
Loc-RIB – common to all peers
Effective-RIB-In
Adj-RIB-Out
List of tables, indexed by AFI-SAFI
Definition of route, augmented by each address-family model
Special application RIB, used for route injection
Note: config  true
bgp-rib.yang
BGP path attributes

## Slide 19: BGP Path Attributes
bgp-message.yang
ORIGIN path-attribute
AS-PATH path-attribute
NEXT-HOP path-attribute
LOCAL-PREF path-attribute

## Slide 20: BGP Internet Routes
Augmentation on top of bgp-rib:routes for IPv4 routes
List of IPv4 routes, indexed
by IPv4 prefix
bgp-inet.yang

## Slide 21: BGP Linkstate Routes
Augmentation on top of bgp-rib:routes for Linkstate routes
List of Linkstate routes, indexed by an opaque route-key
bgp-linkstate.yang

## Slide 22: BGP RIB RESTCONF Endpoints

## Slide 23: BGP-LS Topology Exporter

## Slide 24: Base Network Topology Model
network-topology.yang
List of topologies
List of nodes
List of termination-points on the node
List of links between nodes
Attributes associated with node
Attributes associated with TP
Attributes associated with link

## Slide 25: Network Topology RESTCONF Endpoints

## Slide 26: BGP Topologies
IPv4 Reachability Topology
Node = Next hop IP address, augmented with igp-node-attributes containing list of prefixes that have this next-hop
No TP or Link information
Linkstate Topology
Node = IGP (OSPF) Router
TP = Interfaces on Router
Link = Link between Routers

## Slide 27: Installation
To be execute from Karaf console (can be enabled to run on startup)
  feature:install odl-bgpcep-bgp-all (or install selectively)
Set logging level as desired
  log:set DEBUG org.opendaylight.bgpcep.bgp
  log:set DEBUG org.opendaylight.protocol.bgp

## Slide 28: Configuration
Three ways to configure
  Edit CSS config files (e.g. 41-bgp-example.xml)
  Use Netconf controller-config mount point
    Leads to creation of uber currentconfig CSS file
  Use OpenConfig API
    Limited support in Be, recommended method in Bo+
Configuration steps
  Configure BGP RIB instance
  Configure one or more BGP peers
  Configure Application RIB (optional)
  Tweak other settings e.g. BGP port, capabilities advertised (optional)

## Slide 29: Troubleshooting
Initialization
  Is ODL BGP speaker listening on port TCP/1790?
    Shell: sudo netstat -natp | grep 1790
  Is ODL process running?
    Shell: ps -ef | grep karaf
  Is BGP feature deployed?
    Karaf console: feature:list -i | grep bgp
  Check karaf.log file for initialization errors
Connectivity
  Is the BGP connection between ODL and peer established?
    Shell: sudo netstat -natp | grep 179
  Is ODL BGP speaker running on TCP/179 or is port 1790 fwded to 179?
    Shell: sudo iptables -t nat -L -n
  Is ODL BGP speaker and/or BGP peer able to reach each other?
    Shell: ping <peer-ip-address>
  Is ODL BGP speaker and/or BGP peer able to connect to each other on BGP port?
    Shell: telnet <peer-ip-address> <bgp-port>

## Slide 30: Troubleshooting
Configuration
  Does the BGP connection flap?
    Shell: sudo netstat -natp | grep 179
    Output shows different port numbers when run few minutes apart
  Are BGP speakers configured with correct peer address
    E.g. Check contents of 41-bgp-example.xml config file
  Are BGP speakers configured with correct AS numbers
    E.g. mis-matching AS number for IBGP connection
  Do BGP speakers have mis-matching capabilities
    E.g. ODL supports 4-octet AS numbers only
    E.g. Both speakers should support the same address-families
  Check karaf.log file for negotiation errors

## Slide 31: Troubleshooting
Loc-RIB or Topology do not have expected entries
  Trace the entries in the sequence they are processed
    Adj-RIB-In  Effective-RIB-In  Loc-RIB  Adj-RIB-Out
    App-RIB  Loc-RIB  Adj-RIB-Out
    Adj-RIB-In  Effective-RIB-In  Loc-RIB  example-linkstate-topology
  Use packet sniffer e.g. Wireshark to capture BGP traffic between peers and analyze it

## Slide 32: PCEP

## Slide 33: Overview
Communication protocol for exchange of MPLS Traffic Engineering (TE) information between PCE and PCC
Defined by RFC 5440
Stateful extension to enable synchronization of LSP state between PCC and PCE
LSP management can happen in two ways
  PCE initiated
    LSP is created and controlled by PCE
  PCC initiated
    LSP is created by PCC which may then delegate it to PCE
    PCE can update it only if control is delegated by PCC

## Slide 34: Standards Supported
RFC5440 - Path Computation Element (PCE) Communication Protocol (PCEP)
RFC5541 - Encoding of Objective Functions in the Path Computation Element Communication Protocol (PCEP)
RFC5455 - Diffserv-Aware Class-Type Object for the Path Computation Element Communication Protocol
RFC5521 - Extensions to the Path Computation Element Communication Protocol (PCEP) for Route Exclusions
RFC5557 - Path Computation Element Communication Protocol (PCEP) Requirements and Protocol Extensions in Support of Global Concurrent Optimization
RFC5886 - A Set of Monitoring Tools for Path Computation Element (PCE)-Based Architecture
draft-ietf-pce-pceps - Secure Transport for PCEP
Stateful extensions to the Path Computation Element Protocol, December 2013
  draft-ietf-pce-stateful-pce-07 - PCEP Extensions for Stateful PCE
  draft-ietf-pce-pce-initiated-lsp-00 - PCEP Extensions for PCE-initiated LSP Setup in a Stateful PCE Model
Segment routing extension to the Path Computation Element Protocol, October 2014
  draft-ietf-pce-segment-routing-01 - PCEP Extension for segment routing
  draft-ietf-pce-lsp-setup-type-01 - PCEP Extension for path setup type
draft-ietf-pce-stateful-sync-optimizations-03 - Optimizations of Label Switched Path State Synchronization Procedures for a Stateful PCE
draft-sivabalan-pce-binding-label-sid-00 - Carrying Binding Label/Segment-ID in PCE-based Networks

## Slide 35: BGP-LS and PCE-P
Harvest Network Intelligence
BGP-LS
Program for Optimized Experience
PCE-P

## Slide 36: PCEP Topology Model
network-topology-pcep.yang
Augmentation on top of network-topology:node for PCC information
PCC information comprises of list of LSPs with associated details

## Slide 37: PCEP Topology
Node = Path Computation Client (PCC), augmented with pcep-client-attributes
No TP or Link information

## Slide 38: PCEP RPCs
RPCs for creation and removal of LSP – used by PCE initiated LSP use-case
RPC for updating LSP – in addition to PCE initiated, used by PCC initiated LSP + delegation use-case

## Slide 39: Installation
To be execute from Karaf console (can be enabled to run on startup)
  feature:install odl-bgpcep-pcep-all (or install selectively)
Set logging level as desired
  log:set DEBUG org.opendaylight.bgpcep.pcep
  log:set DEBUG org.opendaylight.protocol.pcep

## Slide 40: Configuration
Two ways to configure
  Edit CSS config files (e.g. 39-pcep-provider.xml)
  Use Netconf controller-config mount point
    Leads to creation of uber currentconfig CSS file
  No OpenConfig model available
Configuration steps
  No special configuration required
  Tweak default config params e.g. PCEP topology name (optional)

## Slide 41: Troubleshooting
Initialization
  Is ODL PCE listening on port TCP/4189?
    Shell: sudo netstat -natp | grep 4189
  Is ODL process running?
    Shell: ps -ef | grep karaf
  Is PCEP feature deployed?
    Karaf console: feature:list -i | grep pcep
  Check karaf.log file for initialization errors
Connectivity
  Is the PCEP connection between ODL PCE and PCC established?
    Shell: sudo netstat -natp | grep 4189
  Is PCC able to reach ODL PCE?
    Shell: ping <peer-ip-address>
  Is PCC able to connect to ODL PCE on PCEP port?
    Shell: telnet <odl-ip-address> <pcep-port>

## Slide 42: Troubleshooting
Configuration
  Does the PCEP connection flap?
    Shell: sudo netstat -natp | grep 4189
    Output shows different port numbers when run few minutes apart
  Is PCC configured with correct ODL PCE address and source address?
    E.g. Check PCC running-config
  Check karaf.log file for negotiation errors
Does PCC show up in ODL PCE PCEP Topology?
  Check LSP delegation config on PCC (PCC initiated)
Is LSP state operationally UP?
  Check path provided in EROs
  Check if PCC is configured currently e.g. MPLS-TE / RSVP config
Use packet sniffer e.g. Wireshark to capture PCEP traffic between PCC & PCE and analyze it

## Slide 43: BMP

## Slide 44: BMP (BGP Monitoring Protocol)
BGP
RR
BGP
BGP
App
BMP
RESTCONF
BMP
RFC 7854
Enables access to peer’s Adj-RIB-In and Effective-RIB-In
You can get a LOT of prefixes

## Slide 45: Installation and Configuration
To be execute from Karaf console (can be enabled to run on startup)
  feature:install odl-bgpcep-bmp
Two ways to configure
  Edit CSS config files (e.g. 42-bmp-example.xml)
  Use Netconf controller-config mount point
    Leads to creation of uber currentconfig CSS file
  No OpenConfig model available
Configuration steps
  No special configuration required
  Tweak default config params e.g. BMP port (optional)

## Slide 46: Flowspec

## Slide 47: Setting “Flows” (FlowSpec)
RFC 5575
Similar to OpenFlow but uses BGP to distribute match/action rules
Matches:
Source / Destination IP prefix
IP Protocol
Source / Destination TCP/UDP port
ICMP Type / Code
TCP Flags
Packet Length
DSCP Field
Fragment (DF, IsF, FF, LF)
Actions:
Rate limit
Traffic sampling
Redirection
Traffic marking (DSCP)
And more... (optional)

## Slide 48: DDoS Mitigation using uRPF and IPv4/IPv6
Point 192.0.2.1/32 to null on all nodes
Turn on uRPF
Advertise routes with next-hop of
192.0.2.1 to discard

## Slide 49: Installation and Configuration
To be execute from Karaf console (can be enabled to run on startup)
  feature:install odl-bgpcep-bgp-flowspec (installed from odl-bgpcep-bgp-all)
No special configuration required

## Slide 50: Thanks